## Slide 1: Socket Communication
CAVLI C10QM MODULE
Anagha Dinesh

## Slide 2: INTRODUCTION
Socket communication is a method to exchange data between devices and servers over TCP/UDP.
Used in IoT modules to connect sensors or devices to cloud platforms.
Controlled via AT commands

## Slide 3: CAVLI C10QM
LTE Cat 1 module with full TCP/IP stack for internet data transfer. Supports AT+QIOPEN and AT+QISEND for opening and sending data over TCP/UDP sockets.
Integrated GNSS and support for multiple Internet protocols for IoT/M2M applications. An optional eSIM with the Cavli Hubble platform enables global connectivity.

## Slide 4: PDP Context Setup
Socket operations need active data connectivity.
Key commands
  AT+CGDCONT=1,"IP","internet" // Define APN
  AT+CGATT=1 // Attach to network
  AT+CGACT=1,1 // Activate PDP context
Sets up PDP context: APN, IP type, and session activation.

## Slide 5: AT+CIPMUX – Multiple Connections
Set single or multiple TCP/UDP connections
Command
  AT+CIPMUX=<connection_mode>
Parameters
  0 – Single connection.
  1 – Multi-connection

## Slide 6: AT+CIPSTART - Open TCP Socket
Establish a TCP or UDP connection to a server.
Command
  AT+CIPSTART=<mode>, <"ip_address"|"domain_name">,<port>,[ssl_flag], [ca_cert_id],[client_cert_id],[prv_key_i d]
<mode> | Connection type: "TCP" for TCP, "UDP" for UDP
<"ip_address“> | Remote server's IP address.
<"domain_name"> | Remote server's domain name (alternative to IP).
<port> | Server port number (1–65535).
[ssl_flag] | 0 – disabled, 1 – enabled
[ca_cert_id] | CA certificate ID
[client_cert_id] | Client certificate ID
[prv_key_i d] | Private key ID

## Slide 7: AT+CIPSEND - Send Data
Transmit data through the open socket.
Command
  AT+CIPSEND=<connection_number>.[<length>] > Your message
  <length>] - A numeric parameter which indicates the length of sending data, it must be less than <size> (1-65536)

## Slide 8: Socket Communication Flow (sample)
Define PDP context: AT+CGDCONT=1,"IP","internet".
Attach to network: AT+CGATT=1.
Activate context: AT+CGACT=1,1.
Set single-socket mode: AT+CIPMUX=0.
Open TCP socket: AT+CIPSTART="TCP","server.com",6800.
Send data: AT+CIPSEND > <message> CTRL+Z.
Close socket: AT+CIPCLOSE.
Shut down stack: AT+CIPSHUT.

## Slide 9: Reference
Cavli C10QM AT Command Manual ERV 1.9